ONTARIO FIRE CODE MAINTENANCE REQUIREMENTS

| DAILY | CHECK | Fire alarm power and trouble lights |
| --- | --- | --- |
| WEEKLY | CHECK | Unsupervised sprinkler control valves |
|  | CHECK | Dry sprinkler system air pressure |
|  | CHECK | Fire protection water supply valves |
|  | CHECK | Hoods, filters, ducts |
|  | TEST | Emergency Generator |
| MONTHLY | INSPECT | Portable fire extinguishers |
|  | INSPECT | Doors in Fire separations |
|  | INSPECT | Fire hose cabinets and stations |
|  | TEST | Emergency lighting |
|  | TEST | Voice Communication Systems |
|  | TEST | Sprinkler alarms |
|  | TEST | Fire Alarm System |
|  | CONDUCT | Fire drill in institutional occupancies |
| TWO MONTHS | TEST | Sprinkler supervisory and waterflow devices |
| THREE MONTHS | TEST | Elevators in High Buildings |
|  | TEST | Smoke control measures in High Buildings |
|  | CONDUCT | Fire Drill in High Buildings |
| SIX MONTHS | TEST | Sprinkler supervisory devices |
|  | SERVICE | Fire suppression systems for cooking equipment |
|  | SERVICE | Emergency generator |
|  | INSPECT | Elevators in smoke shafts in High Buildings |
| ANNUALLY | CHECK | Sprinkler heads |
|  | TEST | Fire alarm system (to ULC S-536 Standard) |
|  | TEST | Emergency lighting for required duration |
|  | TEST | Wet Sprinkler flow alarms and main drain test |
|  | TEST | Dry pipe valves by trip test |
|  | INSPECT | Venting for firefighting in High Buildings |
|  | INSPECT | Air handling systems in High Buildings |
|  | INSPECT | Fire dampers and fire stop flaps |
|  | INSPECT | Chimneys and flue pipes |
|  | INSPECT | Disconnect switches for air handling units |
|  | INSPECT | Fire Hydrants on private property |
|  | INSPECT | Siamese connections and caps |
|  | SERVICE | Fire Extinguishers (to NFPA 10) |
|  | CLEAN | Incinerator spark arrestors |

This list is for convenience only.  Owners are responsible to ensure that all fire safety measures required by the Ontario Fire Code are completed and that written records of all tests, inspections and corrective measures are maintained for at least two years and are available to the fire department on request.